School:  		Course:	 		Instructor:

Student Name:

Date:		 Week:			Block: 			Team:

# Section: 4 Programming

## Lesson: 033: Motor Control

Driving Question:

How can we control the movement of the robot?

Assessment:

| Points Earned | Total Points | ASSESSMENT METHOD |
| --- | --- | --- |
| ASSIGNMENTS: |
|  |  | Vocabulary |
|  |  | Worksheet Assignments/Labs |
|  |  | Course Research |
|  |  | Engineering Journal Entries |
|  |  | Calculations |
| QUIZ/EXAM: |
|  |  | Materials Covered Quiz /Exam |
|  |  | Performance Objectives or Standards Quiz/Exam |
|  |  | Student Generated Quiz |
| PROJECT: |
|  |  | Project Design – Engineering Notebook or Journal |
|  |  | Project Troubleshooting |
|  |  | Program Code |
|  |  | Competition |

Lesson Materials:

##### Activity #33: Motor Control

Background:

What good is a robot with wheels if we can’t drive it around? We can use programs to control the motors which turn the wheels and make the robot move.   In this activity we will learn how to control the motors on the robot.

How do we control each of the motors on the robot?

We have a left and right motor control circuit that we assembled and installed onto the PCB.  We saw on the schematic diagram that each circuit was connected to several pins on the microcontroller. You may recall that there is a clever device called an H bridge used with AND gates to provide a stronger signal to generate power to turn the motors.

Lucky for us someone else wrote the C code that interacts with the pins and the AND gate, and they developed functions that we can just call when we want to turn the motors on and off.  Those functions are in a file called asuro.h that we include with our program.

In this lesson we learn how to use those functions to turn on and off the motors, and control their speed. With these functions we can make the robot move forward and reverse and also turn left and right, and stop.

Concepts:

- Engineers and technicians use technology to solve problems, improve investigations and communicate.

- Understandings about science and technology.  Robots and automated machines are technological inventions based on science and research.

- Science as a human endeavor.  The application of robots:  to help humans solve problems or perform jobs and functions that are dangerous, dirty, or not desired by humans, or require accuracy and speed that most humans cannot sustain.

Performance Objectives:

It is expected that students will:

Computer Science Skills

- Write a program to control the movement of the robot – forward, reverse, turn left and right

- Demonstrate ability to increment and decrement variable values

- Demonstrate ability to define constants

- Demonstrate understanding of datatypes

- Demonstrate ability to assign values to variables

- Demonstrate ability to create loops using for and while statements

- Demonstrate understanding of logic functions for AND, OR, and Exclusive-OR

- Demonstrate ability to use conditional statements and operators

- Demonstrate ability to use switch statements to compare multiple values

- Demonstrate ability to create functions and call them

- Demonstrate ability to use these ASURO functions: MotorDir(), MotorSpeed(), Sleep(), SerWrite(), and SerRead()

Activity Instructions:

##### Complete these steps.   Estimated Time to complete:  60 minutes

- Open worksheet and review:  Activity 33 Worksheet

- Read Chapter 33 Motor Control  in book

- Review the other linked resources

- Download the program code for this activity

- View activity video: Motor Control

- Complete activities in the worksheet

- Complete Assessments

Activity Steps:

With this activity we will learn:

- How do we turn on and off the motors?

- How do we control the speed of the motors?

- How do we turn left and right?

- How do we stop?

- How do we use these ASURO functions?

  - The MotorDir() function

  - The MotorSpeed() function

  - The SerWrite() function

  - The SerRead() function

- How do we write our own functions?

- How do we write a switch statement to compare multiple cases?

Note: By now you know how to copy, save, make, and flash the program so we will no longer repeat those steps.

Part 1:

- Open program: Driving Controlling the Motors

- Write a function to drive Forward for a number of seconds

- Run the program with the Robot elevated so wheels don’t touch.  Use a stopwatch to verify the time is 5 seconds.   Was it close?

- Change the program to run for 10 seconds, and verify, then try 20 seconds.

- Change the program back to 5 seconds.  Download again. Put robot on the floor next to a straight line and see if it runs straight. (in most cases it will not)

- Adjust either the left or right motor speed to compensate so that it runs straight. MotorSpeed(150,150);  Keep modifying the values and trying it until it runs straight.

- Write a function to drive Reverse for a number of seconds.

- Try the program with the Robot elevated so wheels don’t touch.  Use a stopwatch to verify the time is 5 seconds.   Change the program to run for 10 seconds, and verify, then try 20 seconds.

- Change the program back to 5 seconds.  Download again. Put robot on the floor next to a straight line and see if it runs straight. (in most cases it will not)

- Adjust either the left or right motor speed to compensate so that it runs straight. MotorSpeed(150,150);

- Record values below in the questions.

Part 2:

- Write a function to turn Right at 90 degrees

- Write a function to turn Left at 90 degrees

- Modify the main routine to call the right and left turn functions

- Calibrate the motors to make good turns

- Record values  for Motor Speed below in the questions

Part 3:

- Write a program to move in a rectangle shape

- Mark starting point for robot, run the rectangle program, did you end up where you started?

- Tape a pen to the front of the robot (without damaging anything on the robot), run the program on top of a piece of paper.

- Modify the program to change the size of the rectangle.  Draw several rectangles of different sizes.

Part 4:

- Write a program to use the arrow the keys on the keyboard to direct the robot to move forward, reverse, left, and right.

- Use a Switch statement to check for the values of keyboard input.

- Try the program first with the wheels up on blocks until you are sure it works

- Then try the program on the floor.

- Copy and paste the program code below.

Questions:

- Create a list of new vocabulary words and their definitions.

  - Function

  - Switch statement

  - MotorDir()

  - MotorSpeed()

- Record the values from the activity here.

  - Forward

  - Reverse

  - Right Turn

  - Left Turn

  - Rectangle - did you end up where you started?

  - Include a photo of the rectangles your robot drew

  - Were you able to control the robot with the keyboard?

- How is a function defined in a C program? Give an example.

- How is a function activated or called from the main routine? Give an example.

- Provide example code of using a Switch statement to check for values entered on a keyboard.

- How did this activity go for you?

  - What challenges did you overcome and how?

  - What new skills or knowledge did you acquire?

  - Reflect on this activity and write a conclusion.

Project Activities:

- Continue your project design notebook for the ARX ASURO robot.   Create a new sub-Section for Motor Control in the Programming section.

- Insert your program code from the activity.

Programs:

- Insert your program code from the activities here.